## Slide 1: Mathematical Modeling of the Atmosphere – Overview and Examples of Two Current Issues
Donald Dabdub
Department of Mechanical & Aerospace Engineering
University of California, Irvine

## Slide 3: Satellite Observations
Atlantis over the Bahamas – International Space Station 7/10/2011
Photo courtesy of NASA’s Marshall Space Flight Center

## Slide 4: Chamber Studies
EUPHORE
Outdoor smog chamber
One Atmosphere Research
Outdoor chamber
Aerosol Flow System
Indoor chamber
UC Irvine
UNC
Valencia, Spain

## Slide 5: Computational Studies
IBM 1401 computer circa 1960
Photo courtesy of the IBM corporate archive

## Slide 6: Different Types of Models
Numerical Weather Predictions Models
Climate Models
Chemical Atmospheric Models:
  Box Models
  Urban and Mesoscale Models
  Global Chemical Transport Models

## Slide 7: Numerical Weather Predictions

## Slide 8
Global Climate Model

## Slide 9
Global Climate Model

## Slide 10: What is an Air Quality Model?
150 m
1100 m
40 m
0 m
310 m
670 m
80 Cells
30
Cells
123 Gas Species
296 Aerosols: 37 species, 8 sizes
361 Reactions
Each Cell: 5 x 5 km2

## Slide 11: Mathematical Foundation
Source: Dabdub and Seinfeld, Parallel Computing, 22 (1995)

## Slide 12: Modeling laboratory chambers
Source: Knipping et al., Science, 288 (2000)

## Slide 13: Modeling the urban atmosphere
150 m
1100 m
40 m
0 m
310 m
670 m
80 Cells
30
Cells
123 Gas Species
296 Aerosols: 37 species, 8 sizes
361 Reactions
Each Cell: 5 x 5 km2
Source: Vutukuru and Dabdub, Atmospheric Environment, 42 (2008)

## Slide 14: Global aerosol modeling
Sulfate
Source: Rodriguez and Dabdub, J. Geophys. Res., 109 (2004)

## Slide 15: Applications Outline
Hydrogen Fuel Cell Vehicles
  Hydrogen production infrastructure
  Distribution and consumption of hydrogen
Use of Biomass for Biopower vs Biofuel
  Biomass infrastructure for biopower
  Shift from biopower to biofuel

## Slide 16: Central vs. Distributed Generation
Solar
Fuel Cell
Gas Turbine
Microturbine

## Slide 17: Project Overview
Infrastructure scenarios
1100 m
40 m
150 m
0 m
310 m
670 m
80 Cells
100+ Gas Species
20+ Aerosol Species
300+ Reactions
Each Cell: 5 x 5 km2
3-D air quality model
Air quality impacts
?
?
?
?
?
Long Beach
Los Angeles
Riverside
Determine spatial/temporal
emissions
Determine
spatial/temporal
AQ impacts
Determine GHG
co-benefits

## Slide 18: Methodology
Pollutant Emissions
Air Quality Simulations
Technology Scenarios
Baseline Emissions
2005 EPA NEI
Sparse Matrix Operator Kernel Emissions (SMOKE) Model
Spatial Surrogates
Activity Profiles
Chemical Mechanism
Meteorological Fields
Community Multi-scale Air Quality (CMAQ) Model
Dilution, transport and mixing Photochemical transformation
Ozone concentration over a 24 h period in 2005
Emissions of NOx over a 24 h period in 2005

## Slide 19: Hydrogen Fuel Cell Vehicles
What are the requirements for the implementation of FCV?
  Infrastructure for hydrogen production and distribution for fuel cell vehicles
  Hydrogen fuel cell vehicles adoption
How are emissions spatially distributed?
What are the potential air quality impacts?

## Slide 20: Integrated Fuel Cycle Analysis - Hydrogen
Adjust
Contribution
Hydrogen
Generation
Hydrogen
Distribution
Hydrogen
Utilization
Input:
Input:
Adjust
Contribution
Input:
Adjust
Contribution
Input:
Output:
Total
Hydrogen
SMR
Electrolysis –
Grid
SMR
Coal Gasification
Electrolysis –
Renewable
Distributed:
Centralized:
Natural
Gas
Electricity –
Grid
Electricity –
Renewable
Water
Coal
Compression
Liquid Tanker
Compression
Tube Trailer
Pipeline
Compression
Compression
Compression
Liquefaction
Compression
Liquefaction
Vehicle Dispensing
Vehicle Dispensing
Vehicle Dispensing
Vehicle Dispensing
Vehicle Dispensing
Vehicle Dispensing
%
%
%
%
%
%
%
%
%
%
%
%
%
%
GHG emissions
Energy consumption
Criteria pollutant emissions
Water consumption
Notes: At the heart of our assessment methodology is a model that analyzes the performance of an integrated hydrogen supply chain from a life cycle perspective. It includes the generation of hydrogen, hydrogen distribution, and hydrogen utilization.
As an input the model requires some quantity of hydrogen… In the trial cases that we ran, for example, the input was in kg per day of hydrogen based on projected demand in Southern California.
The remaining inputs are to adjust the contribution by each technology to the overall supply of hydrogen.
We have hydrogen generation including both centralized and distributed technologies and the adjusted contribution by each of these technologies also determines the feedstock resources required.
Where hydrogen generation is centralized, distribution is required,
AND regarding dispensing, a variety of pressures for gaseous dispensing are included as well as liquefied hydrogen.
Now this is a simplified schematic of the model. Currently it includes several additional technologies and is friendly to adding more for future studies.
The outputs include GHG emissions, energy consumption, criteria pollutant emissions, and water consumption. The model is adaptable in that more outputs could be included. It is also compatible with existing analysis tools such as the DOE’s H2A model that deals with cost.
I’m going to show you an example of the results, but to do that I’ll first establish a case for the adoption of hydrogen infrastructure.

## Slide 21
Year: 2060 | Scenario-R: |  |  |  |  | Scenario-F: |  |  | 
 | H2 generated from more renewable sources |  |  |  |  | H2 generated from more fossil fuel sources |  |  | 
Population of HFCV | 10,162,500 |  |  |  |  | 10,162,500 |  |  | 
Hydrogen demand (kg/day) | 5,943,730 |  |  |  |  | 5,943,730 |  |  | 
VMT/day by HFCV | 573,807,694 |  |  |  |  | 573,807,694 |  |  | 
Hydrogen Generation | Number of facilities | H2 output (kg/day) | Percent contribution | Location relative to the SoCAB |  | Number of facilities | H2 output (kg/day) | Percent contribution | Location relative to the SoCAB
Centralized |  |  |  |  |  |  |  |  | 
Steam Methane Reforming | 15 | 2,022,285 | 34.0% | Inside |  | 16 | 2,157,104 | 36.3% | Inside
Coal IGCC | 5 | 641,560 | 10.8% | Outside |  | 12 | 1,539,744 | 25.9% | Outside
Petroleum Coke IGCC | 0 | 0 | 0.0% | Inside |  | 2 | 247,466 | 4.2% | Inside
Electrolysis | 7 | 1,905,133 | 32.1% | Outside |  | 7 | 429,196 | 7.2% | Outside
Distributed |  |  |  |  |  |  |  |  | 
Steam Methane Reforming | 155 | 135,700 | 2.3% | Inside |  | 155 | 135,700 | 2.3% | Inside
Stationary Fuel Cell | 2,023 | 736,372 | 12.4% | Inside |  | 2,560 | 931,840 | 15.7% | Inside
Electrolysis | 950 | 305,942 | 5.1% | Inside |  | 950 | 305,942 | 5.1% | Inside
Home or Office Fueling | 39,348 | 196,738 | 3.3% | Inside |  | 39,348 | 196,738 | 3.3% | Inside
Hydrogen Distribution | Distance (km/kg H2) | H2 throughput (kg/day) |  |  |  | Distance (km/kg H2) | H2 throughput (kg/day) |  | 
Remote pipelines | 50 | 2,546,693 |  |  |  | 50 | 1,968,940 |  | 
Urban pipelines | 15 | 3,064,615 |  |  |  | 15 | 3,064,615 |  | 
Liquid tanker | 30 | 1,504,363 |  |  |  | 30 | 1,308,895 |  | 
Hydrogen Refueling |  | H2 delivered (kg/day) | Percent contribution |  |  |  | H2 delivered (kg/day) | Percent contribution | 
140 bar gaseous fueling |  | 4,108,125 | 70% |  |  |  | 4,108,125 | 70% | 
350 bar gaseous fueling |  | 1,760,625 | 30% |  |  |  | 1,760,625 | 30% | 

## Slide 22: GIS Data
Source: Southern California Association of Governments
Central Los Angeles
Notes: 22

## Slide 23: Spatial & Temporal Distribution
Truck Delivery Routes
H2 Fueling Stations
Regional SMR
Regional Petroleum Coke
Central Coal/Biomass
Central Renewable /Nuclear
Local High-Temp Fuel Cells
Distributed SMR
Interstates & Freeways
H2 Pipelines
H2 Truck Deliver Routes
Los Angeles
NV
AZ
CA
Distributed Generation
Southern California
Year: 2050
Land Use
Industrial
Vacant
Oil & Gas Infrastructure

## Slide 24: Results: Ozone
Baseline
Ozone: 8-hour average [Δ Scenario vs. Baseline]
FCV with More Fossil Fuel-based H2
FCV with More Renewable-based H2
Notes: The difference in the two scenarios is in how the hydrogen is produced. See table in the back-up slides. In summary, in the “more renewables” case there is a higher percentage of H2 produced by electrolysis using renewables outside the basin, with respect to the “more fossil fuel” case. In the “more fossil fuel” case, there is a high percentage of H2 produced by gassification of coal, which occurs outside the basin, and gassification of petroleum coke (petcoke), which occurs inside the basin. Petcoke is a by-product of petrochemical processing. It can be used in aluminum and steel industry, or it can be processed to produce fuels. There are large reserves in the Long Beach/Los Angeles petrochemical hub. In terms of air quality, the differences in air quality impacts between the two cases are due to the emissions from H2 production from petcoke. Two plumes downwind from Long Beach can be spotted in the “more fossil fuel” case plot.

## Slide 25: Results: PM2.5
PM2.5: 24-hour average [Δ Scenario vs. Baseline]
Baseline
FCV with More Fossil Fuel-based H2
FCV with More Renewable-based H2
Notes: As explained in the previous slide, the differences in air quality impacts between the two cases are due to the emissions from H2 production from petcoke. There is a spike in PM2.5 emanating from Long Beach that travels northeast in the “more fossil fuel” case plot.

## Slide 26: Use of Biomass for Biopower vs Biofuel
What are the biomass resources?
  Types of biomass available
  Co-location of biomass installations with power and fuel infrastructure
How are biomass resources used?
  Biopower production
  Biofuel production: bio CNG, Ethanol
What are the potential air quality and greenhouse gas impacts?

## Slide 27: Overview of California Biomass Resources
California great biomass resources (CBC, 2011):
  Biopower current capacity: 1200 MW
  Potential additional capacity: > 4,000 MW
Tittmann et al. 2008

## Slide 28: Existing vs Technical Potential
Solid Fuel Technical Potential (MWe)
Source: California Biomass Collaborative, 2011

## Slide 29: Emission Factors
Biogas from wastewater treatment plants, landfill gas, and animal manure
Forest and other solid fuels
1·10-2
2008 ARB limits for DG
2013 ARB limits for DG
ARB BACT for biogas engines
Average CA solid fuel facilities

## Slide 30: Collection and Transport
Include collection and transportation emissions

## Slide 31: Analysis of Full Cycle Emissions
Following ARB’s Low Carbon Fuel Standards Pathways
Using CA-GREET model emissions for well-to-tank processes

## Slide 32: Potential Emissions from Biomass Use

## Slide 33: Spatial Allocation of Emissions
Facilities
Collection and Transport
2020 Technical Potential: NOX Emissions

## Slide 34: Effect of Maximum Biopower Potential
Difference in Max 1-hour Ozone
Difference in 24-hour average PM2.5
Maximum Biopower vs Current Biopower
Notes: Note that this scenario assumes 4 GW of new biopower installed in California, and that central generation is reduced by the same amount. In other words, this scenario assumes a reduction in emissions from central power plants that correspond to 4 GW of power. Considering that there is 60 GW of central generation in the state, the emission reductions from central power generation correspond to a reduction of 6.7% in emissions from power generation. This reduction is only a small fraction of the total emissions from biopower that are introduced in the state. Hence, the negative impacts on emissions and air quality of this particular scenario.

## Slide 35: Effect of CNG vehicles
Maximum CNG vs Current Biomass
Difference in Max 1-hour Ozone
Difference in 24-hour average PM2.5
Notes: Note that this compares current biopower case vs. a case with all technical biomass resources used to produced CNG. CNG from biogas is simply produced by cleaning up the biogas and compressing it. CNG from solid biomass is produced by gasification of biomass, followed by methanation, and gas clean-up.
So the Max CNG case removes current biopower installations, resulting in decrease in emissions and decreases in ozone and PM2.5 in the great parts of the state.
Gasification produces mostly CO, H2, CO2 and H2O. Then the flue gas goes through methanation, which converts H2 and CO into methane:
CO + 3 H2  CH4 + H2O
This is the reverse reaction of steam methane reformation.

## Slide 36: Two-thirds to three-quarters reduction in NOx needed to attain ozone standards
Nitrogen Oxides Emissions in 2023 with Adopted Standards
Additional Needed Emission Reductions
* Source: Ambient ozone modeling conducted by SCAQMD, 2012; final data

## Slide 37: Goods Movement Contribution

## Slide 38: Capabilities
Air Emissions and Air Quality Modeling Tools:
  Systematic and highly resolved methodology to analyze alternative fuels:
    Hydrogen
    Biofuels
    Distributed electricity
  Analysis of criteria pollutants and greenhouse gases emissions
  Potential uses for toxics

## Slide 39: Thanks!

## Slide 40: References
Rodriguez M., Carreras-Sospedra M., Medrano M., Brouwer J., Samuelsen G.S. and Dabdub D., 2006. Air quality impacts of distributed power generation in the South Coast Air Basin of California 1: scenario development and modeling analysis. Atmospheric Environment, 40, 5508-5521.
Carreras-Sospedra M., Dabdub D., Brouwer J., Knipping E., Kumar N., Darrow K., Hampson A. and Hedman B., 2008. Air quality impacts of distributed energy resources implemented in the North-eastern United States. Journal of the Air & Waste Management Association, 58, 902-912.
Medrano, M., Brouwer, J., Carreras-Sospedra, M., Rodriguez, M.A., Dabdub, D., Samuelsen G.S., 2008. A Methodology for Developing Distributed Generation Scenarios in Urban Areas using Geographical Information Systems. International Journal of Energy Technology and Policy, 6, 413-434.
Carreras-Sospedra M., Vutukuru S.K., Brouwer J., Dabdub D., 2010. Air Quality Impacts of Central Power Generation Compared to Distributed Generation in the South Coast Air Basin of California. Atmospheric Environment, 44, 3215-3223.
Vutukuru S., Carreras-Sospedra M., Brouwer J. and Dabdub D., 2011. Future impacts of distributed power generation on ambient ozone and particulate matter concentrations in the San Joaquin Valley of California.. J. Air & Waste Manage. Assoc., 61, 1319-1333
Stephens-Romero S.D., Samuelsen G.S., 2008. Demonstration of a novel assessment methodology for hydrogen infrastructure deployment . International Journal of Hydrogen Energy. 34, 628-641.
Stephens-Romero S.D., Carreras-Sospedra M., Dabdub D., Brouwer J., Samuelsen G.S., 2009. Determining Air Quality Impacts of Hydrogen Infrastructure and Fuel Cell Vehicles. Environmental Science Technology. 43, 9022-9029.
Stephens-Romero S.D., Brown T.M., Kang J.E., Recker W.W., Samuelsen G.S., 2010. Systematic planning to optimize investments in hydrogen infrastructure deployment. International Journal of Hydrogen Energy, 35, 4652-4667.